%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% This is the main code for runing the SMART Robot %
% Author: Yu Gu %
% This is the version with Hukuyo lidar interface %
% The Kinect interface is removed %
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

clear all
close all

% Definitions
Ts_Desired=0.1; % Desired sampling time
Ts=0.1; % sampling time is 0.1 second. It can be reduced
        % slightly to offset other overhead in the loop
Tend=60; % Was 60 seconds;
Total_Steps=Tend/Ts_Desired; % The total number of time steps;
Create_Full_Speed=0.2; % The highest speed the robot can travel. (Max is 0.5m/s)

% Magnetometer Calibration Data
Mag_A=[ 2.3750 0.2485 -0.2296
        0 2.6714 -0.1862
        0 0 2.5061]; % estimated shape of the soft iron effect
Mag_c=[ 0.0067; 0.2667; 0.0473]; % estimated center of the hard iron effect

% Rate Gyro Biases
P_Bias=0;
Q_Bias=0;
R_Bias=0;
% P_Bias=-0.0019;
% Q_Bias= 0.0053;
% R_Bias=-0.0149;

% Define the main Data Structure
SD= struct( 'Index',zeros(1,Total_Steps),... % SD stands for SMART Data, which stores all the robot data
        'Time', zeros(1,Total_Steps),... % The actual time at each time step (s)
        'Time_Diff', zeros(1,Total_Steps),... % The time difference between two step (s)
        'Delay',zeros(1,Total_Steps),... % Delay needed between each time step. It indicate how much time avaliable for other compuations.
        'Lidar_Angle', zeros(682,Total_Steps),... % Hukuyo Lidar Scan Angles
        'Lidar_Range', zeros(682,Total_Steps),... % Hukuyo Lidar Scan Range
        'Logger_Counter', zeros(1,Total_Steps),... % The Counter number for the SMART data logger
        'Ax',zeros(1,Total_Steps),... % Acceleration along the x-Axis (g)
        'Ay',zeros(1,Total_Steps),... % Acceleration along the y-Axis (g)
        'Az',zeros(1,Total_Steps),... % Acceleration along the z-Axis (g)
        'P',zeros(1,Total_Steps),... % Roll Rate (deg/s)
        'Q',zeros(1,Total_Steps),... % Pitch Rate (deg/s)
        'R',zeros(1,Total_Steps),... % Yaw Rate (deg/s)
        'Mx',zeros(1,Total_Steps),... % Magnetic strength along the x-axis (G)
        'My',zeros(1,Total_Steps),... % Magnetic strength along the y-axis (G)
        'Mz',zeros(1,Total_Steps),... % Magnetic strength along the z-axis (G)
        'IMU_T',zeros(1,Total_Steps),... % IMU internal temperacture (C)
        'Roll',zeros(1,Total_Steps),... % Roll Angle (rad)
        'Pitch',zeros(1,Total_Steps),... % Pitch Angle (rad)
        'Yaw',zeros(1,Total_Steps),... % Yaw Angle (rad)
        'Mag_Heading',zeros(1,Total_Steps),... % Magnetic Heading (rad)
        'X',zeros(1,Total_Steps),... % Robot X Position (m)
        'Y',zeros(1,Total_Steps),... % Robot Y Position (m)
        'RF_F',zeros(1,Total_Steps),... % Front Range Finder (mm)
        'RF_FL',zeros(1,Total_Steps),... % Front-Left Range Finder (mm)
        'RF_L',zeros(1,Total_Steps),... % Left Range Finder (mm)
        'RF_B',zeros(1,Total_Steps),... % Back Range Finder (mm)
        'RF_R',zeros(1,Total_Steps),... % Right Range Finder (mm)
        'RF_FR',zeros(1,Total_Steps),... % Front Right Range Finder (mm)
        'Laser_RF', zeros(1,Total_Steps),... % Laser Range Finder (mm)
        'Wall', zeros(1,Total_Steps),... % Wall sensor of Create (0/1)
        'VirtWall', zeros(1,Total_Steps),... % Detect the Virtual Wall (0/1)
        'Dist', zeros(1,Total_Steps),... % Distance Traveled Since Last Call (m)
        'TotalDist', zeros(1,Total_Steps),... % Total Distance Traveled(m)
        'Angle', zeros(1,Total_Steps),... % Angle Traveled Since Last Call (rad)
        'TotalAngle', zeros(1,Total_Steps),... % Total Angle Traveled (rad)
        'CreateVolts', zeros(1,Total_Steps),... % Voltage of the Create Robot (rad)
        'CreateCurrent', zeros(1,Total_Steps)); % Current of the Create Robot (rad)

% Initialize the Serial Port for the Data Logger
S_Logger=Init_Logger('2'); % May be different on different computer
% Initialize the Serial Port for iRobot Create
S_Create=RoombaInit(1);
% Initialize the Serial Port for LightWare Laser Rangefinder
% S_LightWare=Init_LightWare('3');

% Initialize the Serial Port for Hukuyo Lidar
S_Hokuyo=Init_Hokuyo(4); % initalize the Lidar
pause(0.1);
fscanf(S_Hokuyo)
rangescan=zeros(1, 682);
for i=1:Total_Steps
    SD.Lidar_Angle(:,i)=(-120:240/682:120-240/682)*pi/180; % an Array of all the scan angles
end
fprintf(S_Hokuyo,'GD0044072500'); % request a scan

flushinput(S_Logger); % Flush the data logger serial port
flushinput(S_Create); % Flush the iRobot Create serial port
fwrite(S_Create, [142 0]); % Request all sensor data from Create
BeepRoomba(S_Create); % Make a Beeping Sound
pause(0.1);

   turncount=0;
   turnflag=0; %0 for left 1 for right
   SD.thetar=zeros(1,600);
   A=1;
   X_P=0;
   P_P=1;

% Starting the main loop
for i=1:Total_Steps
    tic
    SD.Index(i)=i;

    % Acquire data from the sensor interface board
    if i==1
        [SD.Logger_Counter(i), SD.Ax(i), SD.Ay(i), SD.Az(i), Raw_P, Raw_Q, Raw_R, Raw_Mx, Raw_My, Raw_Mz, SD.IMU_T(i), A2D_Ch1, A2D_Ch2, SD.RF_F(i), SD.RF_FL(i), SD.RF_L(i), SD.RF_B(i), SD.RF_R(i), SD.RF_FR(i)] = Read_Logger_2(S_Logger,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0);
    else
        [SD.Logger_Counter(i), SD.Ax(i), SD.Ay(i), SD.Az(i), Raw_P, Raw_Q, Raw_R, Raw_Mx, Raw_My, Raw_Mz, SD.IMU_T(i), A2D_Ch1, A2D_Ch2, SD.RF_F(i), SD.RF_FL(i), SD.RF_L(i), SD.RF_B(i), SD.RF_R(i), SD.RF_FR(i)] = Read_Logger_2(S_Logger,SD.Logger_Counter(i-1),SD.Ax(i-1),SD.Ay(i-1),SD.Az(i-1),Raw_P, Raw_Q, Raw_R, Raw_Mx, Raw_My, Raw_Mz, SD.IMU_T(i-1), A2D_Ch1, A2D_Ch2, SD.RF_F(i-1), SD.RF_FL(i-1), SD.RF_L(i-1), SD.RF_B(i-1), SD.RF_R(i-1), SD.RF_FR(i-1));
    end
    SD.P(i)=Raw_P-P_Bias; SD.Q(i)=Raw_Q-Q_Bias; SD.R(i)=Raw_R-R_Bias; % Calibrate the gyro data
    temp=Mag_A*[Raw_Mx-Mag_c(1); Raw_My-Mag_c(2); Raw_Mz-Mag_c(3)]; % Magnetometer Raw Data Correction
    SD.Mx(i)=temp(1); SD.My(i)=temp(2); SD.Mz(i)=temp(3);

    flushinput(S_Logger); % Flush the data logger serial port

    % Acquire data from the LightWare Laser Rangefinder
% if i==1
% SD.Laser_RF(i) = Read_LightWare(S_LightWare,0);
% else
% SD.Laser_RF(i) = Read_LightWare(S_LightWare,SD.Laser_RF(i-1));
% end
% flushinput(S_LightWare); % Flush the LightWare Laser Rangefinder serial port

    % Acquire the data from the iRobot Create
    [BumpRight,BumpLeft,BumpFront,SD.Wall(i),SD.VirtWall(i),CliffLeft,CliffRight,CliffFrontLeft,CliffFrontRight,LeftCurrOver,RightCurrOver,DirtL,DirtR,ButtonPlay,ButtonAv,SD.Dist(i),SD.Angle(i),SD.CreateVolts(i),SD.CreateCurrent(i),Temp,Charge,Capacity,pCharge]=Read_Create_2(S_Create);
    flushinput(S_Create); % Flush the iRobot Create serial port
    fwrite(S_Create, [142 0]); % Request all sensor data from Create

    % Acquire data from Hukuyo Lidar
    rangescan = Read_Hokuyo(S_Hokuyo, rangescan);
    SD.Lidar_Range(:,i)=rangescan;
    SD.Laser_RF(i) = rangescan(341); % simulated laser rangefinder using the LIDAR center spot
% plot(rangescan);
% drawnow

    flushinput(S_Hokuyo); % Flush the Lidar serial port
    fprintf(S_Hokuyo,'GD0044072500'); % request a new Lidar scan

    Time=clock; % Mark the current time;
    SD.Time(i)=Time(6); % Store the seconds;
    if i==1
        SD.Roll(i)=atan2(SD.Ay(i), SD.Az(i)); % Calculate the Roll angle based on the gravity vector
        SD.Pitch(i)=atan(-SD.Ax(i)/(SD.Ay(i)*sin(SD.Roll(i))+SD.Az(i)*cos(SD.Roll(i)))); % Calculate the Roll angle based on the pitch vector
        SD.Mag_Heading(i)=atan2(-SD.My(i), SD.Mx(i)); % The initial 2D magnetic heading of the robot
        SD.Yaw(i)=0; % Set the current yaw angle as zero
        Attitude_P=zeros(3,3); % Initialization the error covariance matrix for attitude estimation
        SD.X(i)=0; % Initial Robot X Position
        SD.Y(i)=0; % Inital Robot Y Position
    else % If i>1
        SD.Time_Diff(i)=SD.Time(i)-SD.Time(i-1); % Calculate the time difference between steps
        if SD.Time_Diff(i)<0
        SD.Time_Diff(i)=SD.Time_Diff(i)+60; % Compensate for the minute change
        end
        SD.TotalDist(i)=SD.TotalDist(i-1)+SD.Dist(i); % Calculate the total traveled distance based on the encoder reading
        SD.TotalAngle(i)=SD.TotalAngle(i-1)+SD.Angle(i); % Calculate the total traveled angle based on the encoder reading

        SD.Mag_Heading(i)=atan2(-SD.My(i), SD.Mx(i)); % The 2D magnetic heading of the robot

        [SD.Roll(i), SD.Pitch(i), SD.Yaw(i), Attitude_P] = Attitude_Estimation(SD.Mag_Heading(1), SD.Roll(i-1), SD.Pitch(i-1), SD.Yaw(i-1), SD.Time_Diff(i), Attitude_P, SD.Ax(i), SD.Ay(i), SD.Az(i), SD.P(i), SD.Q(i), SD.R(i), SD.Mx(i), SD.My(i), SD.Mz(i)); % Perform the attitude estimation
        SD.X(i)=SD.X(i-1)+SD.Dist(i)*sin(SD.Yaw(i)-SD.Yaw(1)); % Dead Reconing for X position
        SD.Y(i)=SD.Y(i-1)+SD.Dist(i)*cos(SD.Yaw(i)-SD.Yaw(1)); % Dead Reconing for X position
    end

    %% Put your custom control functions here
    %----------------------------------------------------------
    % Use the following function for the robot wheel control:
    % SetDriveWheelsSMART(S_Create, rightWheelVel, leftWheelVel, SD.CliffLeft(i),SD.CliffRight(i),SD.CliffFrontLeft(i),SD.CliffFrontRight(i));
    SD.thetaL(i)=acosd(900/(SD.Laser_RF(i)-155));
    if i==1
        SD.thetar(i)=0+(SD.R(i)+0.0028)*SD.Time_Diff(i);
    else
        SD.thetar(i)=SD.thetar(i-1)+(SD.R(i)+0.0028)*SD.Time_Diff(i);
    end

    Q=(SD.Time_Diff(i)^2)*2.6312e-5;
    R=10.3413;
    %Prediction
    X_A=X_P-SD.Time_Diff(i)*(SD.R(i)-0.0028)+Q;
    P_A=A*P_P*A'+Q;

    %Measurement update
    H=900*sec(X_A)*tan(X_A);
    y=SD.Laser_RF(i)+R;
    r=y-(900*sec(X_A)+155);
    S=H*P_A*H'+R;
    K=P_A*H'*inv(S);
    X_P=X_A+K*r;
    P_P=1-K*H*P_A;

    SD.ThetaEKF(i)=X_P;

    if turncount<6

        if turnflag==0
        SetDriveWheelsSMART(S_Create, Create_Full_Speed*.2, Create_Full_Speed*-.2, CliffLeft,CliffRight,CliffFrontLeft,CliffFrontRight,BumpRight,BumpLeft,BumpFront);
        if abs(SD.thetar(i)) >= deg2rad(30)
        turnflag=1;
        end
        else
        SetDriveWheelsSMART(S_Create, Create_Full_Speed*-.2, Create_Full_Speed*.2, CliffLeft,CliffRight,CliffFrontLeft,CliffFrontRight,BumpRight,BumpLeft,BumpFront);
        if -SD.thetar(i) <= 0
        turnflag=0;
        turncount=turncount+1;
        end
        end
    else
        SetDriveWheelsSMART(S_Create, Create_Full_Speed*0, Create_Full_Speed*0, CliffLeft,CliffRight,CliffFrontLeft,CliffFrontRight,BumpRight,BumpLeft,BumpFront);
    end
    %----------------------------------------------------------
    %% End of the Custom Control Code

    % Calculate the time left in the constant interval
    SD.Delay(i)=Ts-toc;
    if SD.Delay(i)>0
        pause(SD.Delay(i)); % Kill the remaining time
    end
end
Total_Elapse_Time=SD.Time(Total_Steps)-SD.Time(1) % Calcualte the total elapse time, not counting the minutes
SetDriveWheelsSMART(S_Create, 0, 0, CliffLeft,CliffRight,CliffFrontLeft,CliffFrontRight,BumpRight,BumpLeft,BumpFront); % Stop the wheels
BeepRoomba(S_Create); % Make a Beeping Sound

% Properly close the serial ports
delete(S_Logger)
clear S_Logger
delete(S_Create)
clear S_Create
%delete(S_LightWare)
%clear S_LightWare
fprintf(S_Hokuyo,'QT');
fclose(S_Hokuyo);

save('SMART_DATA.mat', 'SD'); % Save all the collected data to a .mat file
SMART_PLOT; % Plot all the robot data